## Slide 1
Any sufficiently advanced technology is indistinguishable from magic.

## Slide 2: Characteristics and Quality attributes of Embedded System : Characteristics
Application and Domain specific
Reaction and Real time
Operation in harsh environment
Distributed
Small size and weight
Power concerns

## Slide 3: Quality attributes of Embedded System
Operational quality attributes
Response time, Throughput, Reliability,
Maintainability, Security, Safety
Non-Operational quality attributes
Testability and Debug-ability, Evoluability,
Portability, Time to prototype and market,
Per unit and total cost

## Slide 4: Chapter 2:Core of embedded system

## Slide 5: Chapter 2:Core of embedded system
GENERAL PURPOSE AND DOMAIN SPECIFIC PROCESSOR.
MICROPROCESSORS
Architectures used for processor design are Harvard or Von-Neumann
RISC and CISC are the two common Instruction Set Architectures (ISA) available for processor design.
Endianness specifies the order which the data is stored in the memory by processor operations in a multi byte system.
1. Little Endian Processors 2. Big Endian Processors

## Slide 6: Chapter 2:Core of embedded system
GENERAL PURPOSE AND DOMAIN SPECIFIC PROCESSOR.

## Slide 7: Chapter 2:Core of embedded system
Microprocessor and Microcontroller

## Slide 8: Chapter 2: Von-Neumann and Harvard Architecture

## Slide 9: Chapter 2:Little Endian and Big Endian
Byte3 Byte2 Byte1 Byte0

## Slide 10: Chapter 2: store and load memory instructions

## Slide 11: Chapter 2: store and load memory instructions

## Slide 12: Chapter 2: Memory

## Slide 13: Chapter 2: Memory

## Slide 14: Sensors and Actuators

## Slide 15: Sensors and Actuators

## Slide 16: Sensors and Actuators

## Slide 17: Sensors and Actuators

## Slide 18: 7-Segment LED Display Unit

## Slide 19: The 7-Segment LED Display Unit

## Slide 20: Optocoupler

## Slide 21: Optocoupler

## Slide 22: Stepper Motor

## Slide 23: Stepper Motor(Full step, Wave step and Half step)
N
S
B
A
D
C

## Slide 24: 8051 Timers

## Slide 25: 8051 Timers

## Slide 26: Serial Communication(scon register)

## Slide 27: Matrix Keyboard

## Slide 28: Matrix Keyboard

## Slide 29: Matrix Keyboard
For Port 2 the values are currently D3D2D1D0 = 1101. The 0 indicates that a button in the D1 column is pressed.

## Slide 30: PPI-Programmable Peripheral Interface
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1- C upper & C lower are I/O mode 0 – BSR mode | Port A 00-simple i/o mode 01-Handshake mode 1x-bi-directional port |  | Port A 0-O/P 1-I/P | Port C upper 0-O/P 1-I/P | Port B 0-8 bit i/o port. 1-handshake mode. | Port B 0-O/P 1-I/P | Port C lower 0-O/P 1-I/P

## Slide 31: I2C

## Slide 32: SPI

## Slide 33: UART

## Slide 34: RS-232

## Slide 35: RS-232

## Slide 36: USB

## Slide 37: Memory

## Slide 38: SRAM

## Slide 39: EPROM

## Slide 40: RAM

## Slide 41: RAM

## Slide 42: RAM

## Slide 43: RAM

## Slide 44: RAM

## Slide 45: RAM

## Slide 46: RAM
Notes: BYTE Addressable Instruction:
MOV A, #03H
MOV, 20H, A
Bit Addressable Instruction:
SETB 01H
CLR 01H

## Slide 47: ROM

## Slide 48: ROM

## Slide 49: Programming Embedded systems

## Slide 50: Build Process in Embedded systems

## Slide 51: Build Process in Embedded systems
The build process involves three steps:
Compiling
Linking
Locating

## Slide 52: Build Process in Embedded systems: Compiling

## Slide 53: Factors to be considered in selecting a controller
Feature set
Speed of operation
Code memory space
Data memory space
Development support
Availability
Power consumption
Cost

## Slide 54: Watchdog Timer

## Slide 55: Processor and I/O Communication: Programmed I/O
Notes: https://quickcse.wordpress.com/2018/09/10/programmed-io-interrupt-driven-io-dma/
https://www.louiewong.com/archives/137

## Slide 56: Processor and I/O Communication: Interrupt-Driven I/O
Notes: https://quickcse.wordpress.com/2018/09/10/programmed-io-interrupt-driven-io-dma/
https://www.louiewong.com/archives/137

## Slide 57: Processor and I/O Communication: DMA
Notes: https://softwareengineering.stackexchange.com/questions/272470/how-does-a-dma-controller-work

## Slide 58: Interrupts in 8051
TF0 – Timer Zero Overflow (2)
TF1 – Timer One Overflow(4)
INT0 – External Hardware Interrupt Zero (1)
INT1 - External Hardware Interrupt One (3)
TI/RI – Serial Communication Transmit Interrupt and Serial Communication Receive Interrupt (5)
Notes: https://softwareengineering.stackexchange.com/questions/272470/how-does-a-dma-controller-work

## Slide 59: Interrupts registers in 8051
Notes: https://softwareengineering.stackexchange.com/questions/272470/how-does-a-dma-controller-work

## Slide 60: Interrupts registers in 8051
Notes: https://softwareengineering.stackexchange.com/questions/272470/how-does-a-dma-controller-work

## Slide 61: Embedded Operating System
Basics
Tasks
Task States
Notes: https://softwareengineering.stackexchange.com/questions/272470/how-does-a-dma-controller-work

## Slide 62: Embedded Operating System
Scheduler
Scheduling Points
Context Switch
Task Synchronization
Real Time Characteristics
Selection Process
Notes: https://softwareengineering.stackexchange.com/questions/272470/how-does-a-dma-controller-work

## Slide 63: Kernel service of Real-Time Operating System
Process Scheduling
Interrupt Handling
Synchronous Interrupt
Asynchronous Interrupt
Task Synchronization
Time Management (RTC)
Notes: https://softwareengineering.stackexchange.com/questions/272470/how-does-a-dma-controller-work

## Slide 64: EMBEDDED SYSTEMS: INTEGRATED DEVELOPMENT ENVIRONMENT
EMBEDDED IDE
TYPES OF FILE GENERATED ON CROSS COMPILATION
1. List file .lst (page header, command line, source code, assembly listing, symbol listing, module info and warnings and error)
2. Hex file .hex (Types)
3. Preprocessor output file
Notes: https://softwareengineering.stackexchange.com/questions/272470/how-does-a-dma-controller-work

## Slide 65: EMBEDDED SYSTEMS: INTEGRATED DEVELOPMENT ENVIRONMENT
4. Map file .map(page header, command line, CPU details, Input modules, Memory map, symbols table, Inter module cross reference, Program size, Warnings and Errors)
5. Obj file .ob
Disassembler/Decompiler
Firmware Debugging
1.Simulator
2.Emulator
Notes: https://softwareengineering.stackexchange.com/questions/272470/how-does-a-dma-controller-work