## Slide 1: Relative Sizes of Organisms
Human ~ 2 Meters
Egg ~ 400 cm
Frog eggs ~ 2 mm
Eukaryotic cells ~ 10-100µ
Bacteria ~ 1-25µ
Mitochondrion ~ 1µ
Viruses ~ 40 -100 nm
Ribosome ~ 30 nm
Proteins ~ 3-10 nm
Molecules ~ 0.5 - 1 nm
1 meter = 102 cm = 103 mm = 106 μm = 109 nm

## Slide 3: Refraction and Oil Immersion
Refractive Index –
the ability of a medium to
bend light
Maximum Magnification =
1500 X
Limited by the wavelength
of visible light

## Slide 4
Bright field
Dark field

## Slide 5: Dark-Field Microscopy
Modified condenser contains disc in center
Only light reflected by specimen can enter objective
Objects surrounded by halo
Advantage - can see smaller objects like spirochetes, internal structures highlighted
Disadvantage - objects look bigger than they actually are

## Slide 6: Phase Contrast Microscopy
Light passes through annular diaphram
Causes light waves to become “in phase” or synchronized
Advantage - can highlight internal cell structures and details
Disadvantage – none

## Slide 7: Comparison of Light Microscopy
Bright field
Dark field
Phase Contrast
1
2
3

## Slide 8: Immuno Fluorescent Technique
Fluorescent tag (fluorescein) conjugated to Antibodies
Antibodies bind to surface of bacteria
Illuminate with specific wavelength of light (FITC- excite with blue, fluoresces green)
Observe with fluorescence microscope
Used with syphilis spirochete and other organisms

## Slide 9: Confocal Microscopy
Uses Fluorescent tags; multiple colors
Optics allow one to view one plane at a time- no background fluorescence
Computer can “section” specimen one plane (20nm) at a time and re-assemble planes into a 3D image
Used much in Cell Biology and Anatomy

## Slide 10: Electron Microscopy
Uses electron beam in place of light
Magnification up to 100,000 X
Transmission EM shows very fine detail
Scanning EM looks 3D
Disadvantages –
non-living specimen, much processing

## Slide 11: Transmission Electron Microscopy (TEM)

## Slide 12: Scanning Electron Microscopy (SEM)

## Slide 13: Comparisons of Light Microscopes with Electron Microscopes
Compound Light Microscopes Maximum magnification with resolution 1,000X
  Modifications of condenser
    Bright field
    Dark field
    Phase Contrast
    UV Fluorescent Microscopy

## Slide 14: Electron Microscope
Use electron beams focused by magnets and projected on a video screen. Smaller defining source = greater resolving power
Transmission Electron Microscope (TEM) magnifications over 500,000 X. Ultra structure of bacteria observed. First time viruses observed
MOST POWERFUL OF ALL OF THE MICROSCOPES USED FOR INVESTIGATION

## Slide 15: Scanning Electron Microscope
Specimen is coated in such a way as to emit electrons when bombarded with electrons they emit electron energies that are picked up by a collector and a true three-dimension image is presented whereas the transmission (TEM) is only two dimension. Does not magnify images as great as the Transmission Electron Scope